## Slide 1
Cooledge
404190206
Luminous Surfaces in Architecture
Cool 300
LU/HSW Credit = 1 hour
Presented by Your Name Here
Date: July 25, 2019

## Slide 2
Credit(s) earned on completion of this course will be reported to AIA CES for AIA members for either LU or HSW credit. Certificates of Completion for both AIA members and non-AIA members are available upon request.
This course is registered with AIA CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product.
______________________________________
Questions related to specific materials, methods, and services will be addressed at the conclusion of this presentation.

## Slide 3
Learn how luminous surfaces will change the way lighting is incorporated into architecture. Topics include the history and role of luminous surfaces in creating spaces that are more synchronized with the human experience of our environment, standards driving the incorporation of human well-being in design, the applications and design approaches for successfully specifying luminous surfaces into architecture, as well as a look at how luminous ceilings can contribute to acoustic performance.
Course
Description

## Slide 4
Learning
Objectives
Understand the role of luminous surfaces for providing illumination in architectural spaces and the implications for human well-being
Understand the design requirements for luminous surfaces as a source of general illumination
Understand three (3) applications for luminous surfaces in architecture
Understand how luminous ceilings can contribute to acoustic performance
At the end of this course, participants will be able to:

## Slide 5
Courtesy Philips Lighting
Notes: Speaker Notes:
What do we mean when we say “luminous surface”? A luminous surface is one that emits light. The focus of this presentation will be on those luminous surfaces that are built for the purpose of providing illumination as opposed to decoration. Inherently, large surfaces that emit enough light to illuminate a space may also be used to attract attention – particularly in retail environments.
- The Shop at Japan House (London, UK)

## Slide 6
“Just think, that a man can claim a slice of the sun.” – Louis Kahn
Nature Is Filled With Luminous Surfaces
Notes: Speaker Notes:
Our starting point should be the space where people first lived and which has influenced how we experience light. Nature has not only shaped how we see the world but also human physiology and our emotional responses to the environment. Recent understanding of this second point has led to a new way think about the role of illumination in our lives and how that illumination is delivered.

## Slide 7
A New Way Of Thinking About Light
Biological Impact of light
  Increased productivity
  Increased memory function
  Faster reactions
  Better sleep patterns
  (circadian rhythms)
Emotional Impact of light
Improvements in mood
Decreased depression scores
Positive judgement of performance
Preference for “natural” illuminance
Visual Impact of light
Task performance
Object identification and enhancement
Color rendition
Lighting must still deliver the performance required to successfully complete visual tasks
The impact of light on the human experience is a driving force for a fundamental change in the approach to lighting for architectural spaces
Notes: Speaker Notes:
Research that started in the early 2000’s has led to a more detailed understanding of the impact that light has on the human experience. In addition, to being the critical factor in allowing us to see, there is a growing body of evidence that demonstrates that light is important for physiological and emotional well-being.
“Human centric”, “biophiliac”, or “integrative” lighting is rapidly becoming more understood and its role in design becoming increasingly important.
The impact of light on the human experience is a driving force for a fundamental change in the approach to lighting for architectural spaces - one that applies a more holistic approach to designing with light by factoring in Visual, Biological and Emotional needs of a space and it’s occupants.

## Slide 8
Why Is This Important?
A widely quoted study by the Environmental Protection Agency (EPA) published in 2001 found that people spend 87% of their time indoors.
Notes: Speaker Notes:
Most of our waking hours are spent in offices, schools, hospitals, and public spaces that have been designed by a team of creative professionals
And yet lighting is often treated as an engineering exercise in ensuring certain basic technical criteria is met instead of a fundamental component of the how people will experience the space
By their nature, luminous surfaces embody both the technical and human experience aspects of design

## Slide 9
Lighting Must Still Deliver Performance
Quality illumination encompasses many performance characteristics
            Quantity
            Consistency
            Color Rendering
            Visual Comfort (eg. glare control, flicker-free)
Visual
Luminous surfaces create a comfortable environment free of visual clutter
Notes: Speaker Notes:
The most obvious requirement of light is for visual performance. The attributes of quality illumination are well known and apply equally when luminous surfaces are used for illumination.
Visual comfort is one of the key attributes and luminous surfaces inherently offer this feature when applied correctly.
Large luminous surfaces can deliver the right quantity of illumination without the glare that may be present with more concentrated sources or the visual clutter created by suspending indirect luminaires
- Cooledge Project: McGuire Woods – Richmond, VA

## Slide 10
What’s Different About a Luminous Surface?
Biological
For most of human history, we lived outdoors under a large luminous surface …the sky
Our eyes are optimized for this type of illumination
  ipRGC receptors in the human eye largely responsible for the health benefits of light are widely distributed and located in the lower eye
  For this reason, they respond better to large luminous surfaces – especially located above (eg. luminous ceilings)
Notes: Speaker Notes:
By now, most of us have heard about circadian rhythms and their importance to human well-being. There have been a number of studies that show improvements in sleep patterns and alertness by ensuring proper lighting
Other studies have indicated that improvements in productivity and memory can also be attributed to improvements in illumination.
In the early 2000’s a new receptor within the eye was discovered and found to be responsible for non-visual responses to light – those that are related to the physiological effects that impact human well-being.
Unlike the rods & cones that are narrowly distributed at a focal point within the eye to optimize visual tasks, these “ipRGC” receptors are distributed over a wider area and in the lower part of the lining of the eye, indicating that they are designed for receiving light from large areas. This makes sense when you consider that one very large area, the sky, was the primary source of illumination for most of human history.
Although more study is needed to quantify the impact, the conclusion is most likely to be that large luminous surfaces are the best way to supply people with the biological benefits needed for their well-being.

## Slide 11
How You Feel Can Depend on the Illumination You Experience
Emotional
CONTROL
Controlling the environment by adjusting the lighting is the most important aspect of delivering emotional benefits
    Dimming – control over the intensity of illumination
    Tunable White – control over the color temperature of the light
Notes: Speaker Notes:
With the advent of new technologies in both lighting – with LEDs – and control systems, the ability to control one’s environment has become much simpler and more effective.
Flicker free dimming and the ability to tune the color temperature are key attributes for creating environments that evoke positive emotions.

## Slide 12
Luminous Surfaces Light the Way
SURFACE AREA
Luminous surfaces offer the optimal way to deliver the physiological benefits of light, if other attributes are present
CONTROL
Flicker free dimming and color temperature control means light is adaptable to user needs, enhancing well being
QUALITY ILLUMINATION
Luminous surfaces may improve visual comfort, as long as all of the requirements for quality illumination are present
Visual
Emotional
Biological
Notes: Speaker Notes:
To summarize: illumination that is designed for human well-being must consider not only the visual performance but also the biological and emotional aspects.
Luminous surfaces offer an alternative way to provide the high quality light needed – especially visual comfort – but perhaps of equal importance the use of large surface areas have the potential to enhance the biological benefits and when combined with controls form the most compelling way to provide general illumination in architecture.
Cooledge Project: Mayer Brown Law – Chicago, IL

## Slide 13
“Just think, that a man can claim a slice of the sun.” – Louis Kahn
Getty Images
Notes: Speaker Notes:
The scientific understanding of the benefits of using luminous surfaces in architecture may be a more recent occurrence, however the idea has been with us for a long time.

## Slide 14
http://wqhdwall.blogspot.com/2015/01/the-most-beautiful-medieval-stained.html
Notes: Speaker Notes: Bringing Natural Light Inside
While not used strictly for illumination, stained glass in houses of worship brought natural light indoors.
When used on a large scale the impact was stunning.

## Slide 15
Luminous Surfaces In Architecture Circa 1937
Notes: Speaker Notes:
With the widespread adoption of electric lighting, the idea of bringing outdoor lighting indoors by creating luminous surfaces moved on to how it might be done with artificial sources as shown in this study from 1937.
By this time artificial skylights were already being deployed but mostly as a decorative element within the space. In the introduction to the paper this Mr. Lyon states how he is attempting to solve the problems of heat, minimum plenum intrusion, uniformity, efficacy and delivered lumens in a 6 foot square luminous surface with a single 300 watt incandescent lamp. Amazing how the problems of 1937 are not that different from today.

## Slide 16
Ambient Luminescence
" Ambient luminescence produces shadowless illumination. It minimizes form and bulk. It minimizes the importance of all things and people. It suggests the freedom of space and can suggest infinity. It is usually reassuring. It quiets the nerves and is restful”
Richard Kelly
Notes: Speaker Notes:
In 1952, Richard Kelly considered by many to be the founder of modern lighting design defined his “three elemental kinds of light effect” or layers of light including the concept of ambient luminescence. In its ideal form ambient luminescence produces shadowless illumination and a sense of space in the same way nature’s luminous surface provides, in his words, “the uninterrupted light of a snowy morning in the open country.”

## Slide 17
Notes: Speaker Notes:
A little later the idea of creating a luminous surface that replicates the ambient luminescence of the sky was adopted by General Motors for their design studios where the use of glare-free ambient lighting would ensure that the details of automobiles designed in the studio would be authentic when seen in their intended environment: daylight.

## Slide 18
Notes: Speaker Notes:
This idea extended to the end of the design process in the Design Dome. Here the new models were displayed for the press in an environment designed to showcase vehicles as they would appear in the even, non-glare illumination of the sky.

## Slide 19
Notes: Speaker Notes:
Automobiles are still viewed in the context of large luminous surfaces that replicate the natural environment. Unfortunately, up until now, the lighting and technology options available to do this have remained essentially unchanged.

## Slide 20
Luminous Surfaces: The Old Way
Notes: Speaker Notes:
The use of fluorescent tubes strung together was for a very long time the only practical way to achieve the scale and intensity required to emulate the sky.
The constraints placed on design – particularly the need for deep setbacks to achieve uniformity - limited the use of luminous surfaces as the source of general illumination to specialty applications such as designing automobiles

## Slide 21
Notes: Speaker Notes:
LED Technology Enables a New Approach for Luminous Surfaces
The limitations of fluorescent lighting technology are no longer relevant to this discussion. LEDs will be the primary source of light for the foreseeable future.
And their incorporation into architecture in the form of luminous surfaces will overcome the restraints encountered by earlier technologies.
Cooledge Project = Ferrari Maserati of Alberta (Calgary)

## Slide 22
LED Lighting Today
T8 Fluorescent Troffer
LED Troffer
Compact Fluorescent Downlight
LED Downlight
LED Linear Pendant
T8 Fluorescent Linear Pendant
Halogen Tracklights
LED Tracklights
LAMPS
LUMINAIRES
LEDs have changed the technology of lighting but not the way spaces are illuminated.
We are still stuck in a world of bulbs and boxes
Notes: Speaker Notes:
LEDs have delivered on their promise of energy savings and long life – and more recently have caught up to or surpassed traditional sources for quality in most applications.
However, LEDs also arrived with the promise of creating new ways to deliver light to the environment. As of today, the technology inside has changed but the approach to lighting has not.

## Slide 23
Architecture is being driven by the need to create spaces that are…
MORE NATURAL
MORE OPEN
MORE SYNCHRONIZED TO HUMAN WELL-BEING
Courtesy LAVA Architects
Notes: Speaker Notes:
As architects you are being asked to create environments that are more natural, feel more open, and provide an experience that better matches human needs for well-being.

## Slide 24
Architecture is Adopting New Standards for Human Well Being
The impact of buildings
Buildings have a substantial impact on the health and wellbeing of people and the planet. Buildings use resources, generate waste and are costly to maintain and operate. Green building is the practice of designing, constructing and operating buildings to maximize occupant health and productivity, use fewer resources, reduce waste and negative environmental impacts, and decrease life cycle costs.
Why use LEED?
Instant recognition for your building Faster lease up rates Higher resale value Healthier indoor space Lower use of energy, water and other resources Better for building occupants, the community and the environment Enhances your brand and establishes you as a leader in green building
Fitwel is the World’s
Leading Certification System
Committed to Building Health for All
Notes: Speaker Notes:
New standards are rapidly evolving that go beyond energy efficiency by defining requirements to improve human well being.

## Slide 25
WELL v2 Building Standard
“The International WELL Building Institute™ (IWBI™) is leading the global movement to transform our buildings and communities in ways that help people thrive.”
“IWBI delivers the cutting-edge WELL Building Standard™, the leading global rating system and the first to be focused exclusively on the ways that buildings, and everything in them, can improve our comfort, drive better choices, and generally enhance, not compromise, our health and wellness.”
“WELL is a standard for buildings, interior spaces and communities seeking to implement, validate and measure interventions that support and advance human health and wellness.”
Notes: Speaker Notes:
Awareness of the impact of illumination on human well-being is a significant part of those emerging standards for creating environments that promote health and well-being
Most of you have probably heard of the WELL standard. Version 2 was released in 2018 and includes lighting as one of its 11 primary “concepts”
Sound is also a concept and we’ll talk later on about how lighting and acoustics are becoming integrated

## Slide 26
WELL v2 Building Standard: Lighting
The standard defines requirements for the quality and composition of illumination in a variety of categories and combines those with the biological and emotional aspects of lighting design
Notes: Speaker Notes:
Within the lighting concept, the standard defines requirements for 8 characteristics of illumination, including the use of circadian lighting to replicate elements of the natural daylight cycle
In addition to addressing physiological aspects of illumination, the standard also defines minimum requirements for the quality of the light

## Slide 27
Lighting must rapidly evolve to meet the needs of this changing world of architecture
Notes: Speaker Notes:
In order to keep up with architectural trends and building standards, the approach to lighting design and hence lighting products must change and do so rapidly.

## Slide 28
LED Lighting: Evolution vs Revolution
Old Technology >> Old Luminaires
New (LED) Technology >> Old Luminaires
New Technologies >> New Luminaires
Evolution: Points and Lines
Revolution: Luminous Surfaces
Notes: Speaker Notes:
The lighting industry has embarked on an evolutionary path to incorporating new technology that ignores the inherent advantage LEDs bring to applications that make new form factors possible.
A revolution in thinking about design is required

## Slide 29
The next fundamental change in lighting will not be based on technology
The next fundamental change in lighting will be based on its integration into design
Courtesy of VELUX
Notes: Speaker Notes:
Fortunately, the tools required to create the luminous surfaces that enable this change are available and the new revolution in lighting is underway.
The luminous ceiling on the left is supplied by nature, the one on the right by the integration of LEDs with architectural materials into a single full illumination solution.
Projects: Left> Atrium with skylight by Velux in London designed by Foster & Partners; Right > Cooledge Project – 500 W. Monroe, Chicago

## Slide 30
Application & Design Approaches for Luminous Surfaces
Luminous Surfaces for Illuminated Features
Luminous Walls
Luminous Ceilings
This section will cover:

## Slide 31
Applications for Luminous Surfaces
Luminous Ceilings
Luminous Walls
Illuminated Features
Notes: Speaker Notes:
There are three primary applications for luminous surfaces in architecture
  Luminous Ceilings to provide general illumination
  Luminous Walls that contribute to the illumination of a space but also act as a feature unto themselves
  Illuminated Features that provide a focal point within a space to draw your attention

## Slide 32
Luminous Surfaces: Illuminated Features
Design Approach
Specifier takes the lead to coordinate the selection of diffusion materials, millwork (if required) and light source
Key Design Considerations:
Setback Distance
  The distance between the light source and the diffusion material
  A low profile is desirable but requires and understanding of the interaction between the light source and material
Optical Properties of the Diffusion Material
Choice of Light Source
Mockups
Are highly desirable to confirm that the setback distance works for the material/light combination
Notes: Speaker Notes:
Because illuminated features incorporate a huge variety of diffusion materials, it is almost always the case that the specifier will be required to take the lead to ensure a successful outcome.
This entails choosing the material that meets the design intent along with the light source that will provide the best illumination.
There are 3 key design considerations involved in this process
  The setback is the distance between the light source and the diffusion material. It is usually desirable for the setback to be as small as possible to enable a low profile, however, there is a limit to how thin the profile can be that requires an understanding of the interaction between the light source and the material being illuminated
  The optical properties of the material will dictate both the minimum setback and the amount of light needed to properly illuminate the feature
  And of course, the type and quality of the light source itself are critical
For best results a mockup, if possible, will confirm the design
- Cooledge Project = Sk-ii cosmetics “Future X” Smart Store (shanghai, china).

## Slide 33
Luminous Surfaces: Illuminated Features - Diffusion Materials
Key Properties:
Transmission: impacts how bright the feature will be
Masking: impacts how uniform the illumination will appear and/or the setback distance between the light source and luminous surface
Jade
(Vancouver, Canada)
Resin
(Portland, USA)
Perforated Metal
(Chicago, USA)
Onyx
(Washington, USA)
Polymer
(Doha, Qatar)
Large Format Graphics
(London, UK)
Notes: Speaker Notes:
The two important characteristics of diffusion materials for illuminated features are…
  Transmission is a measurement of how much light will pass through a material
  Masking is the degree to which the material diffuse the bright spots from LEDs used as the light source

## Slide 34
Luminous Surfaces: Illuminated Features – Light Source Options (LED)
LED Rope
LED Tape
Edge Lit Panel
Rigid LED Panel
Flexible LED Panel
Typical Use |  | Signage
Uniformity (Large Area) |  | Requires Close Spacing
Illumination Quality |  | Not designed for architectural lighting
Ease of Install (Large Area) |  | Simple method but requires a large number of modules
Field Adaptable |  | Yes.
Typical Use |  | Coves, Linear Accent
Uniformity (Large Area) |  | Requires Close Spacing
Illumination Quality |  | Not designed for architectural lighting
Ease of Install (Large Area) |  | Spacing correctly requires a lot of time
Field Adaptable |  | Yes.
Typical Use |  | Direct View, Low Profile Backlighting
Uniformity (Large Area) |  | Size limitations
Illumination Quality |  | Spec grade has good quality
Ease of Install (Large Area) |  | Multiple panels cannot be connected and require more complex wiring
Field Adaptable |  | No
Typical Use |  | Large-Scale Signage
Uniformity (Large Area) |  | Array pattern results in good uniformity
Illumination Quality |  | Spec grade has good quality
Ease of Install (Large Area) |  | Most panels use connectors designed for factory installation
Field Adaptable |  | No
Typical Use |  | Architectural Features, Large Area Illumination
Uniformity (Large Area) |  | Array pattern results in good uniformity
Illumination Quality |  | Spec grade has good quality
Ease of Install (Large Area) |  | When products with snap connectors are used
Field Adaptable |  | Yes.
Notes: Speaker Notes:
There are a number types of LED-based sources used to illuminate diffusion materials.
Rope and tape light are relatively inexpensive but require figuring out the spacing between the modules or rows to prevent bright spots. To achieve a low profile the spacing has to be tight, meaning a lot of tape or rope is required. And when used for large area luminous surfaces the labor to install becomes impractical.
Edge lit panels are also relatively inexpensive and good for small scale applications where a very low profile is required. However at a large scale, they become complex to install and wire up. Edge lit panels are also heavy compared to other options and not field adjustable .
Rigid LED panels deliver the quality of light needed for architectural features and are uniform at a reasonable setback but are typically not designed for field installation.
On the other hand, spec grade flexible LED panels provide both the quality of light and features designed to allow easy installation

## Slide 35
Light Source Options: Flexible LED Panels
Snap Connectors: mechanical and electrical connection – makes installation simple and fast
Cuttable: allows for field adjustability
Flexible & Light Weight: easier to handle and accommodates curves when required
Notes: Speaker Notes:
Properly designed panels incorporate contractor friendly connections as opposed to the type that are used in factory assembly environments like a sign shop
Since field conditions often don’t match the plans, panels should be field cuttable without impacting uniformity or light output
Flexible panels are inherently light weight and therefore easy handle and install. They can also accommodate curves or round columns that are common in architectural features.

## Slide 36
When Things Go Wrong…
Dots
Stripes
STRIPES: spacing between linear sources was not tight enough for the setback distance
DOTS: Light source was not chosen to match the masking characteristic of the diffusion material
Stripes
Notes: Speaker Notes:
Here are some examples of where the design requirements of luminous surfaces were not met
In the first example, the points of LEDs show through the surface material because the light source was not properly matched to the masking performance of the material
The bottom photos show what happens when a linear source is used without proper spacing for the required setback to achieve uniformity, resulting in massive striping

## Slide 37
Luminous Surfaces: Luminous Walls
Design Approach
Similar to Illuminated Features
Is the wall just a feature or is the primary source of illumination?
Structural coordination is an additional requirement
Key Design Considerations:
Setback Distance
Contribution to Illuminance within the Space
Large Areas dictate solutions that are simple to install
Notes: Speaker Notes:
Just as there is a wide variety of materials used for features, so to for luminous walls and therefore the same guidelines for choosing the materials and light source apply.
In addition, luminous walls are often used to contribute to the illumination of the space and so an additional consideration for how much light is required becomes part of the design process
Because of the sheer size of many luminous walls, light sources that may work on a feature scale are no longer feasible because they are not designed for integration into the building structure
- Cooledge Project = 550 Washtington – Chicago, IL >> Frosted Acrylic + Patterned Aluminum Sheet

## Slide 38
When Things Go Wrong…
More Stripes
STRIPES: the cavity depth (setback distance) was not enough for the fluorescent fixtures used to provide uniform illumination resulting in ugly stripes
Notes: Speaker Notes:
To address the need for high light output and simple installation, fluorescent lighting has often been used for illuminating walls
Here is an example of a luminous wall that used an inexpensive fluorescent lighting solution in a high end retail environment. The spacing of the fluorescent sources was not designed correctly for the available setback distance with an unfortunate aesthetic result.

## Slide 39
When The Right Illumination Source is Chosen…
“I personally think it was a very easy transition from fluorescent bulb to [flexible LED panel]. It is a cleaner look and was fast and efficient to install. It makes the space look better as you see in the pictures of before and after.”
- Christian Plaza - Junior Designer, DDC
Notes: Speaker Notes:
The fluorescent sources were replaced with flexible LED panels resulting in a clean, uniform luminous wall that enhanced the high end furniture on display.
Cooledge Project: Minotti New York by DDC – New York

## Slide 40
Luminous Surfaces: Luminous Ceilings
Non-Stretch Ceilings (Glass, Acrylic, Resin)
Design Approach:
Same as with Illuminated Features and Luminous Walls
Additional Key Design Considerations:
Illuminance Levels
Lighting Power Density (LPD) for energy code compliance
Quality of Illumination
Glass Ceiling
Luminous Stretch Ceiling
Luminous Modular Ceiling
Luminous Stretch Ceilings
Design Approaches:
  (1) Specify stretch ceiling (Div 9) and lighting (Div 26) separately and try to coordinate the design
or
  (2) Specify a full solution that includes specialty installation
Key Design Consideration:
Quality and quantity of illumination
Luminous Modular Ceilings
Design Approaches:
Specify as a luminaire
Notes: Speaker Notes:
There are 3 types of luminous ceilings:
Those that use similar materials to those we have already looked at. In this case, the lighting element becomes even more critical because the luminous ceiling is the primary source of illumination and must fit into the requirements for good lighting design
Luminous stretch ceilings require specialty installers and have the ability to cover very large ceiling areas. Similarly, as the primary source of illumination, the quantity and quality of illumination is the fundamental design feature that needs to be addressed. Stretch ceilings can be specified separately from the lighting, but this approach requires the specifier to manage two separate suppliers operating in two separate construction divisions. A better alternative is to specify a full luminous ceiling solution from a single supplier who will take on responsibility for all of the materials and installation, and ideally will be experts in lighting.
A third approach that delivers the benefits of luminous ceilings but follows more traditional construction processes is to specify large area luminaires that have similar properties to full stretch ceilings but are supplied in a similar way to traditional lighting products.
- Cooledge Projects: Left >> Glass = Audrain Auto Museum (Newport, RI); Middle >> Stretch Ceiling = 500 W. Monroe, (Chicago, IL); Modular = WeWork (Shanghai, China)

## Slide 41
Luminous Ceilings: Stretch Ceilings
2 Types of Stretch Ceiling
PVC (Hot Stretch): the PVC is heated and stretched into place and held with a profile, then tightens to taut when it cools
Knitted/Woven Fabric - (Cold Stretch): the fabric – usually coated polyester – is stretched taut and tucked into profile
Key Design Considerations
Quality of Illumination: luminous ceilings are the primary source of illumination and must deliver the quality and quantity of light required to meet both the technical and human needs of the space
Mounting Type: depending on the type of ceiling and the design intent there are 3 mounting options available.
Notes: Speaker Notes:
There are two types of stretch ceiling that differ in texture and installation process: PVC or “hot stretch” and fabric or “cold stretch”. While they have some different characteristics, the same basic design considerations apply.
As possibly the only source of illumination in the space, it is critical that when working with a stretch ceiling supplier they have the expertise and documentation to confirm the quantity and quality of the light. This includes specifications for all of the lighting qualities including flux, power, IES files, and color quality, etc.
Suppliers of stretch ceilings include installation because it requires specific training and, in the case of PVC, specialty equipment. Installation is also dependent on the mounting type chosen.
- Cooledge Project = 500 West Monroe St. Chicago, IL

## Slide 42
Luminous Ceilings: Stretch Ceiling Mounting Options
Flush Mount
Suspended
Surface Mount
Flush mount solutions are mounted from wall-to-wall across the ceiling or cavity to deliver continuous immersive illumination
Large area luminaires for spaces with higher ceilings or where exposed ceiling elements are part of the design aesthetic
Used to maximize the feeling of openness and volume or to blend with the ceiling finish
Notes: Speaker Notes:
Stretch ceilings can be mounted in 3 ways:
  Flush mount, as the name would indicate, results in a luminous surface that is flush with the ceiling and may stretch across the entire ceiling area or fill a cavity within the ceiling
  Suspended is similar to more traditional pendant mounted luminaires except that the size is generally considerably larger. These solutions are often referred to as clouds and can be as large as the equivalent T-bar ceiling clouds. These are often employed in open concept areas with exposed ceiling elements and can be even more effective if incorporated with acoustic capabilities
  Similarly surface mount luminaires are much larger that traditional luminaires and good for maximizing a feeling of openness in spaces with lower ceiling heights

## Slide 43
Luminous Ceilings: Penetrations
Penetrations
Additional task lighting (downlights)
Notes: Speaker Notes:
An important feature of stretch ceilings is the ability to accommodate the various other elements found in ceilings including supplementary lighting.

## Slide 44
Luminous Ceilings: Penetrations
1. Cut holes in the dust ply and fabric diffuser
2. Press the escutcheon into place until secured
Penetrations
Fire Suppression
Notes: Speaker Notes:
Fire suppression equipment can also be integrated into flush mount ceilings.

## Slide 45
Luminous Ceilings: An Easier Way to Bring the Outdoors…Inside
Suspended
Surface Mount
Recessed
Grid (T-Bar)
Luminous Ceilings in a Traditional Format
Large scale luminaires that provide the benefits of luminous ceilings but in a format familiar to the market
Sizes are typically up to the maximum that can fit through doors and into elevators
Fabric diffusion materials provide the same look and feel as larger stretch ceilings
Mounting methods are the same as traditional luminaires and suitable for most ceiling types
Like traditional luminaires they should have specifications for light quantity and quality including IES files and spectral information
Because specialty installation is not required, there should not be any confusion about which construction division these products will fall into
Luminaires of this type will form the next generation of integrated ceilings
Notes: Speaker Notes:
A recent trend in the market has been to adopt the characteristics of large scale stretch ceilings that make them a superior way to deliver illumination that brings the feeling of the outdoor environment but deliver them in a form factor that is more suited for the traditional construction process
Luminaires are constructed using fabric for diffusion but are sized small enough that they can be shipped complete from the factory and installed by electrical contractors using the same methods as traditional luminaires
As with stretch ceilings, the modular versions enable environments that have the open, natural feel so important to creating a sense of well-being and capitalizing on the emotional and physiological responses that are a fundamental part of our experience
- Cooledge Projects = Top = Bank of America Center – Orlando; Bottom = WeWork - Shanghai

## Slide 46
Applications & Design: Summary
Used to create the feeling of being outdoors in interior spaces, particularly those lacking access to natural light
Stretch ceilings can be specified separately from the lighting but more effective solutions including installation are available from single sources
An easier way to obtain a similar result is to use large-scale fabric luminaires that follow traditional divisions of labor
In either case, illumination should be supplied by lighting experts
Luminous Ceilings
Luminous Walls
Illuminated Features
Primary purpose is as a visual focal point that may also highlight the use of materials to enhance a specific design aesthetic
Uniformity depends on setback and masking
Brightness depends on light output and diffuser transmission
Choice of the light source is critical to success
Encompass all of the design considerations of illuminated features
In addition to creating a focal point the additional intention is to contribute to or provide the illumination within the space
Large Areas dictate solutions that are simple to install
Notes: Speaker Notes:
To summarize:
Luminous ceilings are best specified as holistic solutions supplied from a single manufacturer that understands both ceiling installation and more importantly the properties of light that result in high quality illumination
Luminous walls and illuminated features are dependent on the properties of the diffusion materials in combination with the light source. Flexible LED array panels are the best suited light sources for large architectural features and walls.

## Slide 47
Combining Light & Acoustics
Acoustic Design Issues
Addressing Acoustic Design Using Luminous Ceilings
This section will cover:
Notes: Speaker Notes:
We’ve talked about the impact of illumination on the human experience and how luminous surfaces, in particular luminous ceilings, are ideal for optimizing that experience. But they also can be used to address another aspect of well-being: acoustic design

## Slide 48
Luminous Ceilings: Integrating Light and Acoustics
Noise pollution is a big problem in offices and likely many other public environments
“Studies indicate that approximately 80 percent of office workers believe that their productivity would increase if their working environment was more acoustically private.”
“A 300 percent increase in perceived ‘worker satisfaction’ was reported as a result of the reduction in noise levels from conversational noise. In addition a measured 20% increase in sales productivity was recorded at the end of the six months following the refurbishment.”
American Society of Interior Designers; Armstrong World Industries, Inc.; DynaSound, Inc.; Milliken and Co.; Steelcase, Inc, 2005.
Notes: Speaker Notes:
Whether full stretch ceilings or large area fabric luminaires, luminous ceilings can solve an increasingly important and difficult design problem
Multiple studies have concluded that ambient noise and sound privacy are the two biggest sources of frustration and reduced productivity for office workers.
It is not a stretch to assume that this feeling applies many other public environments..

## Slide 49
Luminous Ceilings: Integrating Light and Acoustics
No walls or glass walls to absorb sound
Stone or tile floors reflect sound
Ceilings are the only place where sound can be absorbed
Combining lighting and acoustic performance can help this
Notes: Speaker Notes:
There are 3 type of noise problems in a given space with corresponding metrics to describe the effectiveness of materials to deal with them
Lighting can help with the problem of reflected ceiling noise that in traditional designs has been addressed by installing acoustic ceiling tile (ACT) ceilings. The relevant material property for this problem is the Noise Reduction Coefficient (NRC) value – a measure of how well a given material absorbs sound
As design moves increasingly toward to open concept spaces, addressing noise issues in other ways than ACT ceilings has become much more important
In open spaces, the trend in design has been to use more durable materials for flooring, however, these materials reflect almost all of the noise back into the space. And by definition, there are very few walls to act as sound absorbers. That leaves the ceiling as the only place to introduce measures to reduce the amount of ambient noise

## Slide 50
Luminous Ceilings: Integrating Light and Acoustics
Combining lighting and acoustics can be unattractive…
Dozens of bright point sources are used to
provide general illumination to make room
for acoustic panels
Lighting and acoustic clouds battle for space, making for a lot of clutter in the ceiling
Funky interior design but the lighting…well….
Downlights are used for general illumination – where’s the “ambient luminescence”?
Combining lighting and sound absorption usually results in compromising the quality of the lighting
Notes: Speaker Notes:
Acoustic panels, baffles, and clouds have typically been used to address this problem
But those solutions occupy the same space needed for lighting
The result is usually not pretty and it is often the quality of the illumination that gets sacrificed

## Slide 51
Luminous Ceilings: Integrating Light and Acoustics
Luminous Ceilings offer a way to do both
Stretch ceilings already offer noise reduction capability…
…so the key to success is ensuring the quality of illumination meets the needs of the people
Notes: Speaker Notes:
One characteristic of stretch ceilings is that most manufacturers typically offer versions that have been designed to absorb sound, sometimes with performance similar to acoustic ceiling tiles
The challenge is that these acoustic solutions typically don’t provide illumination or, once again, sacrifice the quality of illumination to deliver acoustic performance
What has been needed is a lighting solution that provides high quality illumination and simultaneously delivers the sound absorbing properties needed to reduce noise in open spaces

## Slide 52
Luminous Ceilings: Integrating Light and Acoustics
Traditional luminaires have an NRC value = 0 = no sound absorption capability
New acoustic luminaires are finding their way into the market but…
…just as the large scale of Luminous Ceilings provides better general illumination, it also provides better sound absorption capability
The fundamental unit of sound absorption is a “sabin”
A sabin is the product of absorption coefficient x area
Larger size counts as much as NRC value
Acoustic Pendant Luminaire
Acoustic Pendant Luminaire
Modular Luminous Ceiling Luminaire
Notes: Speaker Notes:
Traditional troffer and pendant luminaires that provide the primary layer of illumination contribute nothing to improving noise > the Noise Reduction Coefficient (NRC) value is typically = 0, indicating no sound is absorbed by the luminaire.
Both lighting and baffle manufacturers have recognized the need for combining acoustics and lighting but they suffer from the same fundamental problem we started with at the beginning of this presentation: the limitation of using traditional form factors.
The absorption of sound depends on not just one characteristic – sound absorption of the material as measured by NRC – but a second equally important factor: size
It is the combination of having both high sound absorption properties and large size that make luminous ceilings and large scale modular luminaires the ideal solution for combining light and acoustics to create environments that are good for your eyes… and your ears.

## Slide 53
Applications

## Slide 54
LUMINOUS CEILING
THE SHOP AT JAPAN HOUSE (LONDON, UK)
ARCHITECT Katayama Masamichi, Wonderwall
LIGHTING DESIGN Nulty (London)
INTERIOR DESIGN Marchini Curran Associates
SIZE/AREA 768 sqft (70 m2)
Notes: Speaker Notes:
A stretch ceiling delivers a canopy of light to this retail area of the cultural center

## Slide 55
LUMINOUS CEILING
1 CONAGRA DRIVE (OMAHA, NE)
ARCHITECT Alley Poyner Macchietto Architecture
LIGHTING DESIGN Morrissey Engineering
SIZE/AREA 2100 sqft (195 m2)
Notes: Speaker Notes:
A continuous stretch ceiling continues the flow of natural light from windows at the edge of the atrium into the interior of the space

## Slide 56
LUMINOUS CEILING
STIFEL LAW OFFICE (ST. LOUIS, MO)
ARCHITECT Lawrence Group
LIGHTING DESIGN Randy Burkett Lighting
SIZE/AREA 1300 sqft (120 m2)
Notes: Speaker Notes:
A luminous ceiling acts as the centerpiece of this boardroom giving it the look of a futuristic command center.

## Slide 57
LUMINOUS CEILING
833 CHESTNUT (PHILADELPHIA, PA)
ARCHITECT L2 Partridge
LIGHTING DESIGN L2 Partridge
SIZE/AREA 920 sq.ft (85 m2)
Notes: Speaker Notes:
A series of large flush mount luminous ceiling elements encompasses the corridors of this medical building with high levels of comfortable illumination

## Slide 58
LUMINOUS CEILING
CLOTHING STORE – TIMES SQUARE (NEW YORK, NY)
ARCHITECT In-house Design Team
LIGHTING DESIGN In-house Design Team
SIZE/AREA 9.1’ x 28.5’ (2.8m x 8.7m)
Notes: Speaker Notes:
A large surface mounted luminaire brings the feel of the outdoors to this retail space.

## Slide 59
LUMINOUS CEILING
WEWORK (SHANGHAI, CHINA) – TUNABLE WHITE/ACOUSTIC
ARCHITECT In-house Design Team
LIGHTING DESIGN In-house Design Team
SIZE/AREA 232 sqft (22 m2)
Notes: Speaker Notes:
This modular luminous ceiling incorporates acoustic performance and tunable white to change the mood of the space depending on its use

## Slide 60
LUMINOUS CEILING
BANK OF AMERICA CENTER (ORLANDO, FL)
ARCHITECT HKS
SIZE/AREA 30 Luminaires @ 5’ x 5’ (1.5m x 1.5m) each
Notes: Speaker Notes:
Large scale luminaires are utilized throughout the lobby to provide a signature look for the entire space and to maintain the feeling of natural light in the transition from the outer lobby to the interior elevator and security areas.

## Slide 61
ONE NEW OXFORD STREET – GLASS (LONDON, UK)
ARCHITECT Orms
LIGHTING DESIGN EQ2 LIGHT
SIZE/AREA 1100 sqft (100 m2)
LUMINOUS WALL
Notes: Speaker Notes:
A luminous wall of white fluted glass creates a natural, open experience for people in the lobby of this recently refurbished 1930’s art deco building

## Slide 62
BURJ ALSHAYA OFFICE TOWER – ALABASTER (WHITE ONYX) (KUWAIT CITY, KW)
ARCHITECTS Gensler
KEO International
SIZE/AREA 1100 sqft (100 m2)
LUMINOUS WALL
Notes: Speaker Notes:
This massive white onyx luminous wall is a focal point of the lobby area of this office tower

## Slide 63
IBEW UNION HALL – GLASS (CHICAGO, IL)
DESIGN/BUILD Wight & Company
SIZE/AREA 1300 sqft (120 m2)
LUMINOUS WALL
Notes: Speaker Notes:
An enormous luminous wall contributes to the illumination of this hall and provides a stunning backdrop for speakers

## Slide 64
ILLUMINATED FEATURE
ZABEEL HOUSE HOTEL – LOBBY BAR (DUBAI, UAE)
ARCHITECTS WS Atkins & Partners
ATK Engineering
LIGHTING DESIGN Neolight
Notes: Speaker Notes:
Illumination is used to draw attention to the eclectic design of this lobby bar

## Slide 65
ILLUMINATED FEATURE
FENWICK – ESCALATOR (BRACKNELL, UK)
ARCHITECTS HMKM (London)
RFK Architects
LIGHTING DESIGN Nulty (London)
Notes: Speaker Notes:
Large scale perforated features add visual interest to an otherwise plain element above the escalators in a high end department store

## Slide 66
ILLUMINATED FEATURE
BOTTEGA VENETA GINZA (TOKYO, JP)
ARCHITECT Not Credited
Notes: Speaker Notes:
Luminous surfaces are not restricted for interior use
The store occupies a six-storey building with a façade clad in 900 sqm. (9,688 sq.ft.) of silver panels that collectively mimic Bottega Veneta‘s trademark intrecciato technique of interweaving leather punctuated with illuminated highlights to compete with the surroundings

## Slide 67
“Architecture which enters into a symbiosis with light does not merely create form in light, by day and at night, but allows light to become form” – Richard Meier
Getty Images
Notes: Speaker Notes:
In conclusion: spaces no longer have to suffer from the limitations of traditional form factors that that have restricted us to points and lines of light.
Light will become integral to the structure in the form of the surfaces that define the space.

## Slide 68
This concludes The American Institute of Architects Continuing Education Systems Course
Contact: Presenter Name