## Slide 1
Cooledge Lighting
COOL 500
A Holistic View of Illumination
Presented by Your Name Here
Date: September xx, 2024

## Slide 2
Credit(s) earned on completion of this course will be reported to AIA CES for AIA members. Certificates of Completion for both AIA members and non-AIA members are available upon request.
This course is registered with AIA CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product.
______________________________________
Questions related to specific materials, methods, and services will be addressed at the conclusion of this presentation.

## Slide 3
New standards and increased understanding of the impact of design on human well-being are driving changes in what factors must be considered when choosing lighting.
This course explores the concept of holistic illumination, focusing on the aspects of lighting and sound that are important for ensuring spaces are supportive of wellness and the requirements for addressing them.
In addition, holistic illumination includes the need for various layers of light to be integrated together and explores the role sustainability plays in making design decisions.
Course
Description

## Slide 4
Learning
Objectives
Understand the emerging factors of lighting that require a more holistic view of illumination which includes human well-being, sustainability, and integration
Understand the problems associated with human well-being that need to be addressed during design and how luminous ceilings can provide solutions
Understand the key metrics used to determine the impact of lighting and acoustics on people and their interaction with each other
Understand the current and future state of sustainability in general and specifically as it relates to lighting
At the end of this course, participants will be able to:

## Slide 5
“The quality of a visual environment considers a wide range of variables including…
luminance balance
color appearance
visibility of multiple visual tasks (often accomplished by a layered lighting system made up of ambient/task/accent)
visual comfort
daylight and views
control
user acceptance as a metric
- GSA P100
The Facilities Standards for the Public Buildings Service (P100) establishes mandatory design standards and performance criteria for GSA-owned buildings. Design and construction professionals must abide by the policy and technical criteria in P100.
Notes: Speaker Notes:
General Services Administration P100 requirements apply to federal civilian buildings which provide workspace for 1.1 million federal employees. The GSA is one of the largest real estate holders in the United States.
The view expressed in the P100 document is an example of taking a more holistic view of lighting.
In this course, we are going to look at factors beyond even those noted here.

## Slide 6
Traditional Lighting Factors
Visual Performance
Emotional Response
Energy Consumption
Emerging Lighting Factors
Well-being
Sustainability
Integration
Holistic Illumination
Notes: Speaker Notes:
Light and lighting design has in the past been focused on functionality and creating emotional responses.
These aspects remain critical to success.
Ensuring there is an appropriate amount of light for certain tasks or delivering designs that encourage shopping, socializing, or studying are still the primary activities of lighting design.
However, an additional requirement to consider lighting in the context of well-being is gaining prominence and is likely to become an equal component alongside the others.
In addition to all of that, design teams are being tasked with ensuring sustainability – whatever that means (More on this later)
Finally, the complexity of combining all of these aspects of lighting is leading toward a need for more integration especially as it relates to acoustic performance but also the various layers of lighting, controls, and adjacent mechanical systems.

## Slide 7
Traditional Lighting Factors: There’s Still Work to Do
Visual Performance
Older workforce requires higher light levels
Emotional Response
Tunable White illumination is now affordable
How do we balance the need for more light with ever decreasing allowable energy consumption limits?
How do we take advantage of this feature most effectively?
“Importantly, a company, architect, designer, manager or business leader, motivated to create inclusive spaces for all individuals in an office environment, must concern themselves not with an imagined “average” person, but instead with the nuance of individual differences and preferences.”
  - Tony Esposito, WELL Building Director, Standard Development, Light Concept Lead
Energy Codes
LEDs are pretty efficient. What now?
Will ever more stringent codes result in lack of choice or poor quality illumination?
Notes: Speaker Notes:
The focus of this course is on those emerging factors but before we go there, I’d like to highlight a few challenges related to what we’re calling “traditional” factors that will require more work and more answers on the part of the lighting industry and its partners in design
The relationship between lighting and visual performance is well understood and has a vast set of metrics to define performance.
We also know that the population is aging and with it a need for more light. More inclusive approaches to design also recommend creating spaces that cater to the needs of people at the limits of performance rather than the average.
How will we balance the needs of the people with the desire to reduce energy consumption?
Are LEDs now an efficient enough light source that we can focus on the type and quality of lighting, or will energy codes eventually restrict lighting to only the most efficient methods even if not the best for the people using the space? (For reference, the dark green states enforce the most up to date energy codes while the white ones don’t have statewide codes at all)
Up until recently, tunable white options for LED-based lighting have come with a significant price premium. Now that this is often not the case, how will we best take advantage of this feature to create better lighting experiences?
As I said, we’re not going to try to answer these questions, but they are important enough that they shouldn’t get lost and should be considered alongside the emerging factors impacting lighting design.

## Slide 8
Emerging Factors: (Acoustic) Lighting for Well-Being
What is Driving the Emergence of Well-being as a Design Factor?
What Do People Really Need to Feel Better?
The Characteristics of Lighting that are Important for Well-being
The Importance of Sound Control and How Luminous Ceilings Make a Difference
This section will cover:
Notes: Speaker Notes:
You’re likely familiar with most of them but as a starting point, we are going to quickly review the organizations and emerging standards that are driving changes in what aspects of lighting are important
From there we will look more specifically at how the lighting industry is starting to embrace the idea that lighting has a significant impact on wellness and define what type of lighting is “good for people”
Now that acoustic lighting is a real thing, we’re also going to look at what makes luminous ceilings a better alternative for providing both good lighting and noise reduction

## Slide 9
“We now know that developers and architects can be more effective in achieving public health goals than doctors in white coats.”
- Dr. Richard Jackson from the University of California Los Angeles School of Public Health as quoted in Workdesign.com: How Office Design Can Influence Employee Health and Wellness (2022)
Notes: Speaker Notes:
That’s a pretty heavy load to carry…

## Slide 10
There Are Lots of People Telling You What to Do
Notes: Speaker Notes:
And there are a lot of organizations telling you what to do
Some like LEED started out focusing on efficiency and have expanded to encompass all aspects of building design.
Others like WELL – as the name suggests - are specifically targeted at well-being
Others are even more expansive. LBC regulates the impact on neighboring buildings, who is involved in the construction, and how the building is operated in addition to extraordinary detail about the content of products and where they came from.
One of the biggest challenges designers face is that these standards are changing rapidly, making it difficult to keep up.
For example, even as LEED is transitioning from V4.0 to V4.1, they have published V5.0 that contains significant changes in the requirements for points

## Slide 11
And There Are Lots of Points to be Scored
Notes: Speaker Notes:
And there are lots of points to be scored
A common approach is to award points for specific design features in a variety of categories that when added together will result in a building that addresses the needs of its occupants
This is a significant added burden on you, the designer.
(And even moreso on manufacturers, but that is another topic for another day)
So why bother?

## Slide 12
Designing For The Needs Of People Is Mandatory For Success
“Wellness continues to be a key consideration for companies and landlords when building or redeveloping office spaces.”
- CBRE Online Article 2019
“Wellness in the workplace has emerged as a critical issue because it is simply too fundamental to be ignored.”
“Bodies of evidence from all parts of the globe prove that well designed workplaces are critical for the health and wellbeing of society. The message to the real estate and built environment sector is clear: prioritise health and wellbeing by making spaces human again”
“…More than a ‘fad’ this is a global socio-political shift – rue the industry that is not moving to address it.”
- Cushman Wakefield, Well Work Place: Making Spaces Human Again
“The workplace is the physical manifestation of your company’s culture and core values. By better understanding the deep connection between the human experience and real estate, organizations can create more innovative workplaces that drive productivity, experience and business value.”
- Ed Nolanm, JLL Workplace Strategy
Notes: Speaker Notes:
It is your clients who recognize the value of designing for wellness, driving changes, and supporting new standards.
Here we show examples of large property management firms’ thoughts prior to 2020. The pandemic has added urgency and created an environment where designing for the needs of workers is no longer an option for companies hoping to attract workers back to the office. It is a mandatory requirement.
But offices aren’t the only places where a wellness focus is at the forefront. Greater awareness by the general public can affect almost any public space.
Healthcare has always had a focus on the patient experience but struggled to overcome traditional construction practices. The industry will be forced to adopt new ways to address new design requirements
Hospitality and institutional buildings will also need to cater to people who have gained a sudden awareness and appreciation for spaces that address more than merely functional needs.

## Slide 13
New and emerging building standards recognize the need to provide occupants with environments that have been designed for more than functionality – requiring a number of features be addressed including good lighting and good acoustic performance
New Standards Recognize the Need for Better Environments
Notes: Speaker Notes:
These new and evolving standards provide a useful framework for defining and rewarding projects that are built with human well-being as a central focus.

## Slide 14
Designing For The Needs Of People Is Mandatory For Success
Up to 90%
Percentage of business costs related to employees
Notes: Speaker Notes:
But realistically, how many of your clients are asking for LEED or WELL or LBC or any of the others? For some of you they may represent the majority – especially if you are involved in a lot publicly funded projects. But for many of you, the certification aspect may not be a consequential part of your business
However, the goal of designing for human well-being is still a worthy one because for most businesses, whether office-based, retail, hospitality or others, it is their people who are the most important contributor to their success.

## Slide 15
But What Do People Actually Need to be Healthy and Productive?
Most Important Design Impacts on Users
Air
Light
Water
Temperature
Nature
Sound
Emotional wellness: Give employees access to natural light, and quiet rooms where they can comfortably focus on their work.
Physical wellness: Provide people with healthy food options, and ergonomically designed workstations.
Environmental wellness: Make sure your workspaces have adequate air quality, light, temperature, and proper acoustics.
Notes: Speaker Notes:
So what do people actually need to be healthy and productive?
The study cited in the Harvard Business Review article is based on workplaces but again, the results can be applied to most public spaces.
Designing spaces for humans ultimately comes down to a handful of categories that the design team has control over
And lighting plays a substantial role in determining whether or not an indoor environment contributes to the health and well-being of its occupants

## Slide 16
The Whole Room
LIGHT
Notes: Speaker Notes:
As noted previously, ensuring visual requirements are met and creating the desired emotional responses are fundamental to lighting design, however, emerging factors that address a wider segment of the population and consider the physiological impact are gaining in importance and may soon be equally relevant

## Slide 17
User concerns reported in recent US Department of Energy L-Prize research mirror the latest US Workplace Census reporting.
What’s the Problem?
Poor quality lighting can result in significant problems for large proportions of the population
A survey of migraineurs and control subjects on triggers for migraine and headache found light flicker to be the most cited trigger; it was chosen by 45% of the migraine group compared to only 6% of the control group.
The same migraine group also identified other visual triggers, such as computer screens, glare, abrupt transitions in light conditions, or patterns of stripes
Notes: Speaker Notes:
A workplace census in 2020 highlighted how important having the right lighting can be. Of the problems associated specifically with lighting, having enough light to see properly – especially for those with vision challenges – and poor quality lighting causing headaches and migraines stand out.
Perceived causes were light flicker – now given the fancy name Temporal Light Modulation – and discomfort glare.
The solutions to these problems are relatively simple by selecting the correct type of lighting and ensuring the quality of the products selected.

## Slide 18
CIE Integrative Lighting: Position Statement
𝗕𝗮𝗹𝗮𝗻𝗰𝗲𝗱 𝗟𝗶𝗴𝗵𝘁𝗶𝗻𝗴 𝗤𝘂𝗮𝗹𝗶𝘁𝘆: Emphasizes the need to harmonize human well-being in all its aspects with energy, environmental, and architectural considerations.
September 2024: The CIE is excited to announce the release of the third edition of its Position Statement on Integrative Lighting - "𝗥𝗲𝗰𝗼𝗺𝗺𝗲𝗻𝗱𝗶𝗻𝗴 𝗣𝗿𝗼𝗽𝗲𝗿 𝗟𝗶𝗴𝗵𝘁 𝗮𝘁 𝘁𝗵𝗲 𝗣𝗿𝗼𝗽𝗲𝗿 𝗧𝗶𝗺𝗲."
Since its inception in 1913, the CIE has become a professional organization and has been accepted as representing the best authority on the subject and as such is recognized by ISO as an international standardization body.
𝗣𝘂𝗯𝗹𝗶𝗰 𝗚𝘂𝗶𝗱𝗮𝗻𝗰𝗲: Today, we know enough about the effects of lighting on health to provide general guidance to the public, which the CIE, in collaboration with other international partners, will offer in the coming months.
𝗗𝗲𝘀𝗶𝗴𝗻 𝗖𝗼𝗻𝘀𝗶𝗱𝗲𝗿𝗮𝘁𝗶𝗼𝗻𝘀: Urges careful design to avoid glare and manage lighting energy use while achieving high-quality integrative lighting.
𝗚𝘂𝗶𝗱𝗮𝗻𝗰𝗲 𝗼𝗻 𝗟𝗶𝗴𝗵𝘁 𝗘𝘅𝗽𝗼𝘀𝘂𝗿𝗲: International experts meeting in Manchester, UK, recommended a healthy daily light exposure pattern for young adults: high light exposure during the day, a much lower level for the three hours before bed, and near-darkness during sleep.
𝗖𝗜𝗘 𝗦 𝟬𝟮𝟲:𝟮𝟬𝟭𝟴 𝗖𝗼𝗺𝗽𝗹𝗶𝗮𝗻𝗰𝗲: Characterizing light for integrative effects should adhere to the CIE S 026:2018 standard, the CIE System for Metrology of Optical Radiation for ipRGC-Influenced Responses to Light.
Notes: Speaker Notes:
Now that LED lighting has addressed energy consumption significantly, the focus of the lighting industry is turning to the impact light has on human well-being and how we can balance all aspects of lighting instead of focusing “blindly” on efficacy, the lighting equivalent of miles per gallon
The CIE is the global body tasked with providing guidance and standards to the lighting industry. In general, the regional bodies like the Illumination Engineers Society of North America (IESNA) follow the lead of the CIE and incorporate its input into their own standards and design guidance
In September 2024, the CIE released an updated statement on what they call integrative lighting by which they are meaning, lighting that impacts human physiological responses.
It calls for the inclusion of well-being as a primary consideration alongside energy, sustainability, and aesthetics in lighting design
The reference to ipRGC-influenced responses just means that lighting design should take into account physiological effects including circadian impacts – see next
Managing glare has always been an issue but it now embedded in new standards as is the requirement for high quality lighting in general
And finally, after years of saying “we’re not sure yet” the CIE and other standards bodies think there is enough knowledge available to guide other professionals and the public on the effect lighting has on human well-being

## Slide 19
IES RP-46: What Does It Say About Lighting for Well-being?
Healthy daily light exposure pattern
Large diffuse area lighting
Indirect lighting with white ceilings
Wall washing of light-colored surfaces
Temporal Light Modulation (TLM)
It’s talking about flicker
Known to cause headaches and migraines
Don’t do use products that flicker!
Glare
Possibly another contributor to headaches, etc.
Recommendation: “Large number of lower-intensity luminaires can produce physiologically effective light in a workspace more comfortably than a small number of high intensity products”
Luminous ceilings are this concept at its extreme
Notes: Speaker Notes:
In North America the IES has also recently published guidance on supporting lighting that includes consideration of human physiological responses and best practices for addressing them.
Ensuring an appropriate level light exposure is recommended with guidance that large diffuse area lighting and/or use of wall surfaces are preferred ways to achieve this
The Recommended Practice also addresses the need to ensure flicker falls outside the range of human response and that glare is managed – again noting the use of large, diffuse sources as a preferred method

## Slide 20
Physiological (Circadian) Impacts
A substantial amount of research in the past decade has determined…
Light exposure has a significant influence on our circadian systems which in turn affects:
Sleep
Health
Alertness
Key Characteristics of Circadian Lighting
Amount of light at the right time of day
Spectral qualities of the light
Illuminance at the eye
These receptors are the primary way humans process physiological stimulus from light
In 2020, UL released DG 24480, Design Guideline for Promoting Circadian Entrainment with Light for Day-Active People.
  “Lighting isn’t just for vision anymore. It’s high time we had a valid, agreed-upon metric and some basic guidelines so that healthy lighting can be effectively delivered to benefit society.”
  - Dr. Mark Rea, Ph.D. Professor of cognitive science at the Lighting Research Center (LRC) at Rensselaer Polytechnic Institute
Notes: Speaker Notes:
Both the CIE and IESNA highlight the topic of light exposure.
The past decade has seen a huge increase in our understanding of the role of light on circadian rhythms and associated health impacts.
In particular how light exposure patterns affect sleep, overall health, and alertness.
One of the researchers instrumental in the advancement of our knowledge and helping create design guidelines, Dr. Mark Rhea, states that “Lighting isn’t just for vision anymore”
This topic is more suited to a separate, or several separate, CEU presentations, so for the purpose of this one, we will summarize by noting that the key characteristics of circadian lighting or integrative lighting, are
  Ensuring the right amount of light at the right time of the day
  The spectral qualities of the light – meaning how much blue and/or red does the light contain
These are characteristics that fall directly within the expertise of your lighting designer.
  The third one, illuminance at the eye, is also a lighting design issue, but is also highly dependent on the overall design of the room including colors and finishes, and also whether or not traditional forms of lighting are used or alternatively, whether luminous surfaces are incorporated as part of the integrated design.

## Slide 21
What Kind of Lighting is Best for People?
For most of human history, we lived outdoors under a large luminous surface …the sky
Our eyes are optimized for this type of illumination
  ipRGC receptors in the human eye largely responsible for the health benefits of light are widely distributed and located in the lower eye
  For this reason, they respond better to large luminous surfaces – especially located above (eg. luminous ceilings)
Notes: Speaker Notes:
In the early 2000’s a new receptor within the eye was discovered and found to be responsible for non-visual responses to light – those that are related to the physiological effects that impact human well-being.
Unlike the rods & cones that are narrowly distributed at a focal point within the eye to optimize visual tasks, these “ipRGC” receptors are distributed over a wider area and in the lower part of the lining of the eye, indicating that they are designed for receiving light from large areas. This makes sense when you consider that one very large area, the sky, was the primary source of illumination for most of human history.
Subsequent research has found that to increase the impact of light exposure it is the amount of light reaching these receptors that is critical and that luminous areas in the ceiling or vertical illuminance generated by illuminated walls or walls with diffuse but highly reflective materials are better for this purpose than traditional methods of illumination.

## Slide 22
What Kind of Lighting is Best for People?
EML = Equivalent Melanopic Lux
mEDI = melanopic Equivalent Daylight Illuminance (CIE approved method/RP-46 reference method)
Example of manufacturer data
Notes: Speaker Notes:
Luminous surfaces ensure an effective delivery method to the receptors in the eye
But the other key aspect of lighting for wellness is the spectral characteristics of the light
Some of the standards such as WELL V2 shown here require calculations of melanopic or daylight illuminance which takes into account the amount of the light received combined with spectral distribution - which stimulates a physiological response.
Again, another topic worthy of its own CEU but the key takeaway is that manufacturers should be able to provide spectral data in a format that can be used in the tools designers have available, or even better provide a ratio that can be applied to regular illuminance values to yield the equivalent.

## Slide 23
What Kind of Lighting is Best for People?
No Effect Flicker
Luminous (Stretch) Ceiling
Luminous Ceilings are Low Glare
IEEE 1789: No Effect Level
Notes: Speaker Notes:
A more direct factor required for suitable lighting is to ensure that glare and flicker are reduced to the point where they are not a factor.
Glare is inherently an issue with LED-based fixtures because LEDs are themselves small, very bright sources of light.
Traditional linear, troffer, and point source fixtures have to be properly designed to ensure they minimize glare
In addition to being an ideal way to improve receptivity to circadian effects, because of their diffuse nature, large luminous surfaces are inherently low glare.
A metric used to measure glare is the Unified Glare Rating, or UGR. A value in the range <17-19 is considered the borderline of acceptability. The chart shown here shows that a typical luminous ceiling generally falls within the “barely perceptible glare” range

## Slide 24
Light and Color
It is well known that colors have specific influences on moods and emotions
It is the job of the designer to determine the appropriate colors for the space
It is the job of the lighting within the space to accurately render the desired color and provide the appropriate level of warmth`
Notes: Speaker Notes:
As designers you are well aware that color can play a significant role in enhancing the design vision but also how people perceive and experience a space.
It is the expertise of the design team that will ensure an appropriate palette.
Critical to success however will be in choosing lighting that faithfully renders that palette and sets the baseline level of warmth depending on the desired mood or atmosphere required
Where change is required, whether daylight cycles, seasonal cycles, or the ability to switch from work to socializing, tunable white options are common and generally not as cost prohibitive as once perceived.

## Slide 25
Light and Color
LED-based sources are notorious for having low R9 values
High blue & green content in LEDs can make skin look greenish and unhealthy if enough red is not available
Fun Fact:
Sea water filters out red, so if you are diving at deep levels and cut yourself, your blood will actually look green.
Reflectance Properties of Blood
Notes: Speaker Notes:
Generally, discussions about color rendering,. whether CRI or new metrics, revolve around making objects look better. For example, the red apple or the blue car look better when you use a high CRI light source.
High CRI sources tend to be those optimized for selling merchandise
Very much related but not as much of a consideration is the color rendering of people by the general lighting in the space
LEDs are notorious for not rendering saturated red very well as measured by the R9 color rendering value and for retail and related applications designers generally consider the R9 value. There are two other R values, R13 and R15 that are associated with skin color.
Interestingly, R9 is also important for making people appear healthy because that is partly based on being able to highlight the blood in the skin. Without red in the light, people will appear a little grey.

## Slide 26
In Summary: The Kind of Lighting That is Best for People is…
Light that renders color well and is the correct color temperature for the desired outcome
Light that enhances human physiological responses
Light that has low glare
Light that does not flicker
In other words:
Luminous ceilings with good color rendering characteristics, no perceptible flicker, and suitable spectral content
Notes: Speaker Notes:
And so the answer to what kind of lighting is best for people…
Is large luminous surfaces to optimize the response of the eye’s receptors that have been designed to deliver the right amount of light at the right time of the day
Light that has low glare
Light that doesn’t flicker
And finally, lighting that faithfully renders the designer’s color palette, desired ambiance, and the appearance of the people using the space
A very good option is to use luminous ceilings and as an added bonus, they can also contribute in a meaningful way to solving another problem: Noise

## Slide 27
The Whole Room
SOUND
SOUND
Notes: Speaker Notes:
Just as the impact of lighting on human wellness is becoming a key consideration for building design, the focus on improving the acoustic performance of public spaces is increasing

## Slide 28
“Just think, that a man can claim a slice of the sun.” – Louis Kahn
What’s the Problem?
“Studies indicate that approximately 80 percent of office workers believe that their productivity would increase if their working environment was more acoustically private.”
“A 300 percent increase in perceived ‘worker satisfaction’ was reported as a result of the reduction in noise levels from conversational noise. In addition, a measured 20% increase in sales productivity was recorded at the end of the six months following the refurbishment.”
American Society of Interior Designers; Armstrong World Industries, Inc.; DynaSound, Inc.; Milliken and Co.; Steelcase, Inc, 2005.
Noise pollution is a big problem in offices, educational, and some healthcare environments
Notes: Speaker Notes:
Yet another study done in conjunction with association of interior designers found that sound issues were ranked as THE most important sources of dissatisfaction in workplaces and was able to demonstrate increases in satisfaction and productivity when the noise levels were reduced.
Again, while this study focuses on the workplace, the issue of noise pollution is a problem found in almost any public space

## Slide 29
What’s the Problem?
“Evidence has shown that noise, especially sound with information, such as human voices, can significantly affect office employees' cognitive performance and subjective feelings. Another study found that office noise may cause harm to human health.”
Effects of acoustic environment on design work performance based on multitask visual cognitive performance in office space (2021)
Notes: Speaker Notes:
Not only does noise decrease satisfaction and productivity, there is evidence to suggest that it also has a more direct negative effect on health.
The quote mentions office employees, but imagine the impact in a classroom setting where students face a barrage of unwanted noise, often continuously
Or a crowded museum space where the distraction of noise might significantly reduce the enjoyment of the experience

## Slide 30
Sometimes the Soundscape is About More Than Comfort
“Most retail sound is inappropriate and accidental, even hostile, and it has a dramatic effect on sales”
- Julian Treasure*
He references studies showing that the right “soundscape” in a retail store can increase sales up to 38%.
Conversely, inappropriate soundscapes filled with unwanted noise can decrease sales by 28%.
*Julian Treasure is a sound and communications expert whose TED talks have been viewed over 100M times.
Notes: Speaker Notes:
The ability to design for sound is not just about health. In retail applications it can have a huge impact on sales – both positively and negatively
Julien Treasure is an expert on sound and communications.
He sites research that demonstrates that designing a positive soundscape can dramatically increase sales.
But,.. he also has found that most sound is not controlled with the result that noise can reduce sales almost as dramatically.
The key takeaway from all these studies seems to be that ensuring your space has good acoustic performance is high on the list of requirements

## Slide 31
3 Types of Noise Problems
There are 3 types of noise problems:
  Sound that is transferred through walls/barriers
  Sound that travels from one room to the next through the ceiling plenum
  Sound that bounces off the ceiling and reflects back into the space
Notes: Speaker Notes:
There are three ways that sound may be propagated to increase noise:
  Through the walls
  Through a ceiling plenum that acts as a sound conduit
  Or by reflections off of the ceiling
Managing sound that is transferred through walls is more of a structural design challenge outside of the scope of this discussion.
Ceiling attenuation might be improved using some of the techniques we touch on here, but our main focus is on absorbing noise that reaches the ceiling so that it is not reflected back into the space
To ensure better acoustic performance, taking advantage of as much of the surface area of the ceiling as possible seems like a logical approach

## Slide 32
Acoustic Lighting: Size Matters
Acoustic engineers use a metric called a “sabin” to quantify sound absorption.
A higher sabin value means more sound absorption... equals less noise.
The noise reduction capability of a light fixture is dependent on TWO equally important characteristics:
  1. Absorption Characteristics (often approximated by NRC)
    AND
  2. Absorption Area
Sabin = Absorption x Area
Noise reduction requires good sound absorption properties AND a large surface area to deliver useful noise reduction and create a comfortable environment
The paper towels to the left have the same absorption characteristics
VS
Whole Roll = More Sabins
Single Sheet = Less Sabins
Notes: Speaker Notes:
It’s often the case when we are talking about acoustic performance of light fixtures that we focus on the absorption characteristics of the materials that will be used.
For example, looking at NRC or more intentionally the specific sound absorption properties across the relevant frequencies
But equally important is the amount of area dedicated to sound absorption
A single sheet of paper towel has the same absorption properties as the whole roll. But how much liquid does it absorb in comparison?

## Slide 33
Acoustic Lighting: Size Matters
More Sabins
Less Sabins
Notes: Speaker Notes:
Acoustic luminous ceilings are the roll whereas typical pendants and similar solutions are more like the single sheet of paper towel.
Both incorporate sound absorbing materials but only a luminous ceiling has the ability to have a meaningful amount of noise reduction without adding passive acoustic elements.
And if you think about it, having to add those additional elements sort of negates the purpose of using acoustic lighting

## Slide 34
Why the Frequency of Absorption is Important
Acoustic Design Requires a Detailed Understanding of Absorption at Different Sound Frequencies
Different materials absorb sound at different frequencies
Two materials could have the same NRC value but absorb sound very differently
Most architectural spaces are concerned with the ability to hear speech – e.g. “speech intelligibility”
As shown, the frequencies of interest are those between ~100Hz – 4000Hz
Notes: Speaker Notes:
While the surface area dedicated to acoustic materials is critical, that does not mean we should ignore the properties of those materials.
NRC values can give you an idea about the average material properties, but they are not used by acoustic designers who are more interested in the absorption characteristics across a range of sound frequencies.
For architectural acoustic design, the frequencies most of interest are those associated with human speech - which determines the speech intelligibility of a space. Or in other words, how clearly you can hear someone speaking to you against a background of noise that is most often the sound of other people speaking.
For these applications, it is the ability of materials to absorb sound in the range of 100Hz to 4000Hz that is of interest.

## Slide 35
Notes: Speaker Notes:
This short example attempts to demonstrate the impact of using acoustic materials in a space.
Acoustic performance is generally measured using reverberation time with a lower value indicating quieter space.
Speech intelligibility is an indicator of how well a person can comprehend what another is saying and is generally better within a quieter space.
In this simulation, the addition of a luminous ceiling decreases reverberation time significantly
Adding acoustic materials to the walls reduces the time even further to make a once loud room into a quiet space

## Slide 36
Large Area Acoustic Lighting Enables More Interesting Designs
Stone/Tile Floors
Great for durability, aesthetics, and low maintenance
But…sound is almost completely reflected back into the space
Notes: Speaker Notes:
Incorporating large area acoustic lighting in the ceilings of your spaces offers plenty of area to create a comfortable soundscape and frees you up to use great looking, highly durable floors even though they can be some of the worst materials acoustically speaking

## Slide 37
Large Area Acoustic Lighting Enables More Interesting Designs
Let’s Not Do This Anymore!
Notes: Speaker Notes:
Incorporating acoustic luminous surfaces allows you to create spaces that don’t have to rely on traditional design staples like carpeting, ceiling tiles, troffers, drywall, etc.

## Slide 38
In Summary…
Using the ceiling as the primary sound absorbing surface enables better alternatives for the floors and walls
Noise reduces productivity and satisfaction and may negatively impact health
Noise can reduce sales
Sound absorption relies on area and so acoustic lighting should be applied to large areas of the ceiling
In other words:
Reducing noise is important for well-being and to maximize the effectiveness of acoustic lighting, large area sources should be used
Notes: Speaker Notes:
To summarize…
Noise reduces productivity and satisfaction, and studies indicate that it probably is bad for our health
If you’re doing a retail store design, keep in mind that sound can be good… but often it is very bad
Take advantage of the entire area of the ceiling to increase the acoustic comfort in your space
Try new things. They may surprise you.

## Slide 39
Applications Where Lighting for Well-being is Important
A Few Examples of Applications Where Lighting for Well-being is an Important Consideration
This section will cover:
Notes: Speaker Notes:
The next few slides are some examples where the wellness aspects of lighting may be more important than in other applications.

## Slide 40
Applications Where Lighting for Well-Being Matters: Workplaces
Luminous surfaces deliver comfort with high levels of low glare illumination…sometimes mimicking nature itself
Notes: Speaker Notes:
Most of the data we have looked at was based on workplaces and since so many people spend a significant amount of their time at their workplace it seems self evident that some consideration for their well-being is warranted.
Recently there has been a move by some of the famously large companies to reduce or eliminate working from home, so having the right kind of illumination may grow in importance

## Slide 41
Applications Where Lighting for Well-Being Matters: Workplaces
Taking advantage of tunable white lighting enables workplaces to match daily rhythms
Notes: Speaker Notes:
Tunable white lighting generally no longer comes with the large price premiums of the past and offers the option of creating office environments that match the natural daily rhythms.

## Slide 42
Applications Where Lighting for Well-Being Matters: Libraries
Meeting the visual needs of people in libraries is a no-brainer but bookworms need healthy daily light exposure too.
And aren’t libraries supposed to be quiet? Lighting that absorbs a lot of sabins will help.
Notes: Speaker Notes:
Read the slide…

## Slide 43
Applications Where Lighting for Well-Being Matters: Fitness Facilities
Luminous Ceiling made by Humans
Luminous Ceiling made by Nature
Wellness is a huge part of the fitness experience – the right kind of illumination makes a significant contribution
Notes: Speaker Notes:
Fitness facilities are another application where impact of the lighting has the potential to enhance or detract from the experience.
While dynamic color lighting and loud music are appealing for certain fitness facilities, the ability to bring the feeling of nature to workout and yoga areas can be a big selling feature for operators

## Slide 44
Applications Where Lighting for Well-Being Matters: Education
Providing the right kind of illumination has been linked to increases in alertness and productivity. Acoustic luminous ceilings can provide this and help keep the noise down at the same time.
Notes: Speaker Notes:
Similar to the importance of workplaces, schools would seem to be one of the critical applications for implementing lighting that supports wellness.
A holistic approach to illumination would by definition, contribute to less noise, better conditions for learning, and the opportunity to improve the wellness of young people.

## Slide 45
Designing for Well-being in Education: Another Certification
“Thanks to CHPS hundreds of schools in our district serving thousands of students deliver healthier indoor environments, better daylighting and acoustics, and are more comfortable. These factors make a big difference in how students perform in the classroom and boosts their overall wellbeing when they are at school.”
— Christos Chrysiliou, Director of Architectural and Engineering Services for the Facilities Services Division of the LA Unified School District and CHPS Board Member
School facilities received a D+ on the Report Card for America’s Infrastructure, and it’s estimated that 53% of public schools need to invest in repairs, renovations, and modernizations now to put buildings in good overall condition
- Collaborative for High Performance Schools
Notes: Speaker Notes:
And because there aren’t enough organizations and certifications to worry about, here’s another.
This one does have the worthy cause of trying make school buildings better for all students and provides a framework for doing so.

## Slide 46
Sustainability: A Growing Part of Holistic Illumination
What does sustainability mean in practice?
This section will cover:
Considerations for the future
Notes: Speaker Notes:
We are going to explore each of air, light, sound, and nature to look at what aspects of each are relevant to designing for human well-being and why
We’ll also look at the design requirements and suggest some alternative solutions that address problems and also add value that isn’t included in traditional approaches

## Slide 47
Sustainability: What Does It Mean?
Corporate Level
Focused on Sustainable Business Practices
Limited Demand for Certification
Product Level
Focused on Specific Properties of Products
Vast Variety of Demand for Certification
Notes: Speaker Notes:
There are two levels of sustainability.
The first occurs at the corporate level and looks at the business practices of the manufacturer to determine if it is operated in a sustainable and responsible manner covering environmental footprint and sustainable sourcing but also ethics and treatment of its employees.
It has been our experience that certification at this level has almost no influence on whether products are specified.
The other level focused on the specific properties of products is much more prevalent in the building products market with a large number of organizations offering their own guidelines and certifications.

## Slide 48
Sustainability: What Does It Mean?
LEED and others offer points for submitting a minimum number of EPDs for products that are specified
Specifiers ask for EPDs from manufacturers as a way to score points for their clients’ projects where building certification is a requirement
EPDs offer the opportunity to standardize documentation requests
Follows a standard format (ISO 14025) for creating an EPD based on product information.
3 elements required to create an EPD
  Product Category Rule (PCR)
  Life Cycle Assessment (LCA)
  Environmental Product Declaration (EPD)
Notes: Speaker Notes:
The industry seems to be converging on using Environmental Product Declarations or EPDs as proof of sustainability.
LEED in particular seems to be a big driver of this approach.
For those of you not aware of how EPDs are created, it is a 3-step process based on ISO standards that define the required methods and contents.
The first step is to establish a Product Category Rule that is applicable to a specific type of product and defines the inputs and outputs that must be included
The second step is a Life Cycle Assessment that generally includes a calculation of embedded carbon including transport from suppliers to factories and delivery to customers
The third step is the creation of the EPD document itself which can be done by the manufacturer but scores more points if done by an accredited 3rd party

## Slide 49
Sustainability: What Does It Mean for Lighting Today?
“Environmental Product Declarations (EPDs) are a way for manufacturers to take comprehensive, third-party-verified LCAs, which are quite complex, and turn them into standardized declaration labels for their products.”
“An EPD reports a specific set of environmental results, which can only be created after a full LCA is conducted. Common impact categories include: global warming potential (GWP), ozone depletion potential, acidification potential, eutrophication potential, smog formation potential, and primary energy use.”
“An EPD will have certain characteristics:
  Compliance with ISO standards
  Adherence to the appropriate industry-standard PCR
  Third party certification of the LCA process
  A clear description of the functional unit
  A list of the life cycle stages considered in the analysis”
Status Product Category Rule for Luminaires as of October 2024
Notes: Speaker Notes:
The idea behind EPDs is that they will standardize the sustainability information provided by manufacturers to enable specifiers and customers to compare products.
As it relates specifically to lighting here are some challenges to be aware of.
Lighting manufacturers are being asked for EPDs more frequently however, the Product Category Rule on which they should be based is still in development. That means that any EPD supplied a by a lighting manufacturer is necessarily based on their own assumptions about what should be included.
A second challenge that may extend beyond lighting is that there do not appear to be any correct answers. For example, how much embedded carbon is too much? Should it be measured per lumen? Per area? Etc
While requiring an EPD from a lighting manufacturer is perhaps premature, it is not unreasonable to ask for product composition data or for a manufacturer to address specific questions you may have.

## Slide 50
Sustainability: Where is it Going?
Released for Public Comment in April 2024
LEED V5.0
Requirements are bundled into broader categories with more ways to achieve them
Larger selection of documentation and certification
More products will be required to have documentation/certification
Requirements only apply to non-structural materials
EPDs are one way of many to provide sustainability documentation
Notes: Speaker Notes:
While the PCR that enables lighting EPDs is still in development, LEED appears to be expanding the type of documents and certification that will score points.
The table shown here is from V5.0 that was released in April for public comment.
So, while everyone agrees that sustainability is part of the consideration for inclusion in specifications, the regulatory framework for lighting is still in development and the overall regulatory environment is changing rapidly.

## Slide 51
Sustainability: What Does It Mean for Lighting in the Future?
Today there is a big focus on product recyclability at end of life
And for some segments where the useful life of the space is 7-10 years that is a good conversation
But…
Most LED-based lighting products have a useful life measured in decades
What does “recyclable” look like in 20 or 30 years?
In 2010, was anyone thinking about what to do with LEDs?
LED technology wasn’t a consideration <15 years ago.
What will lighting look like 15 years from now?
Source: Statista
Notes: Speaker Notes:
One last thought about the topic of sustainability
Under the category of sustainability there has been a lot discussion about recyclability.
This makes a lot of sense for spaces with a comparatively short lifespan – retail and office TI’s come to mind.
As a manufacturer, however, committing to recyclability for products that may be installed for 20 or 30 years is a challenge.
For reference, most lighting products on the market today are based on LED technology that from a market perspective really didn’t even exist less than 15 years ago.
The takeaway here is not so much about facts as something to ponder if you find yourself in a discussion about what happens at the end of the product life.

## Slide 52
In Summary…
Everyone agrees that sustainability is a requirement (and hence part of a holistic view of illumination), however, measurement and enforcement are very much a work in progress
There are two levels of sustainability assessment: corporate and product
Environmental Product Declarations (EPDs) are becoming the default assessment tool for sustainability.
The Product Category Rule (PCR) for lighting is still in development
In other words:
A holistic view also looks at the manufacturer as well as the product and while sustainability is desirable, evaluating it is a challenge for specifiers and manufacturers alike
Notes: Speaker Notes:
To summarize…
Read the bullets as they appear

## Slide 53
Integration: Achieving Holistic Illumination
What does integration mean in the context of holistic illumination?
What are the elements of an integrated system?
This section will cover:
Notes: Speaker Notes:
Earlier we reviewed recent statements by the CIE about “integrative lighting” by which they mean the physiological element of lighting.
We are using the term “integration” in a much broader sense.
It is the idea that in order to achieve all of the goals of holistic illumination including both visual performance and well-being, a new integrated approach to lighting will be required.

## Slide 54
Integration: Combining Existing Functions into One
The most successful technology of today is the integration of many earlier successful technologies
Notes: Speaker Notes:
Historically, the idea of combining several technologies that were successful on their own together into a single solution has proven to be a revolutionary way to advance the way we live and do things
Check your pocket – or your hand – for the most obvious example

## Slide 55
Integration: Combining Existing Functions into One
The most successful technologies are the combination of many earlier successful technologies
Notes: Speaker Notes:
Or this one…

## Slide 56
Integration: Combining Existing Functions into One
To supply a complete lighting solution, an integrated ceiling must provide the “three elemental kinds of light effect”
Richard Kelly
What is integration in the context of holistic illumination?
Ambient Luminescence
Play of Brilliants
Focal Glow
Notes: Speaker Notes:
So what does that mean for lighting?
Richard Kelly is regarded as one of the founders of modern lighting design. He defined the “three elemental kinds of light” which are often implemented as “layers of lighting”

## Slide 57
Integration: Luminous Ceilings ARE Ambient Luminescence
" Ambient luminescence produces shadowless illumination. It minimizes form and bulk. It minimizes the importance of all things and people. It suggests the freedom of space and can suggest infinity. It is usually reassuring. It quiets the nerves and is restful” – Richard Kelly (1952)
Luminous Ceilings deliver…
The Kind of Lighting That is Best for People
Light that renders color well and is the correct color temperature for the desired outcome
Light that does not flicker
Light that has low glare
Light that enhances human physiological responses
Notes: Speaker Notes:
Ambient luminescence is the background general lighting that as Kelly defines as shadowless and suggesting a freedom of space
Luminous ceilings are the very embodiment of the concept of the natural ambient luminescence on which he based his definition
As summarized earlier, luminous ceilings have the ability to enhance human responses, and deliver the comfortable, reassuring light that quiets the nerves and is restful
In other words, the kind of lighting that is best for people.

## Slide 58
Integration: Adding Focal Glow & the Play of Brilliants
What are the important factors?
Integrated Controls
Accommodation for site variances
Wiring simplification
Mechanical integration
Minimizing the intrusion into space >> e.g. seamless/hidden visual appearance
Ability to support a variety of linear and point source lighting types: spots, floods, wallwashers, grazers, linear, etc.
Notes: Speaker Notes:
But spaces would be very dull if we didn’t add the other two elements of light: the focal glow and the play of brilliants
Or in more straightforward terms accent lighting and/or decorative lighting
An integrated lighting solution is one that combines the three elements or layers into a single solution that includes control and takes advantage of unique properties of each type of lighting
Such a system would also enable simpler wiring and ideally minimize the intrusion into space by creating a more seamless visual appearance

## Slide 59
Integration: Combining Existing Functions into One
The next revolution in lighting will be the integration of many earlier successful technologies
Notes: Speaker Notes:
An integrated solution then starts with a luminous ceiling incorporating the best lighting technology and sound absorption for wellness along with controls
Additional accent lighting is then added
But why stop at lighting? Other ceiling elements can be incorporated such as speakers, security cameras, sensors, and as already done with stretch ceilings, fire suppression sprinklers
Like the smartphone and smart speaker the result is a solution that represents a leap forward in the art and science of lighting

## Slide 60
Integration
SOUND
LIGHT
CORPORATE RESPONSIBILITY
PRODUCT SUSTAINABILITY
Notes: Speaker Notes:
But to truly achieve holistic illumination, an integrated luminous ceiling system must also meet the needs of the people and the planet
Holistic illumination also means sourcing from companies that meet a high standard for sustainable practices
And products that are sustainable – however that is defined.

## Slide 61
Integration
Notes: Speaker Notes:
Integrated luminous ceilings might be used to enhance public spaces in the workplace or hospitality

## Slide 62
Integration
Notes: Speaker Notes:
Or provide a full lighting solution for retailers looking to create immersive experiences for their customers.

## Slide 63
Traditional Lighting Factors
Visual Performance
Emotional Response
Energy Consumption
Emerging Lighting Factors
Well-being
Sustainability
Integration
Holistic Illumination
Notes: Speaker Notes:
We started out defining holistic illumination as a combination of traditional and emerging lighting factors
Holistic illumination is not a new thing….It’s the next thing.

## Slide 64
This concludes The American Institute of Architects Continuing Education Systems Course
Contact: Presenter Name
Notes: Speaker Notes:
Thank you.